## Slide 1: EDES 301 PCB Project
Juan Aizprua

## Slide 2: Background Information
What is being proposed?
A gadget that can be added to water bottles that allows you to track your intake of water throughout the day and can tell you if you need to drink more or if you’re right on track.
  Pictures
  Links to existing projects / libraries
hidratespark.com/products/hidratespark-pro-32oz-smart-water-bottle
  us.water.io/
  hackster.io/Teenenggr/bottle-that-keeps-you-hydrated-fdf535
  hackster.io/magicbit0/smart-water-bottle-with-magicbit-99f64a
  hackster.io/mweber17/smart-water-14cb33
What improvements / additions over existing project
  Make it available to use on any water bottle with some initial set up. Planning on keeping track of water volume with a water level sensor .Some user interaction so they can check if they are on track either through an application on their computer or pressing a button on the gadget on bottle.

## Slide 3: System Block Diagram
Initial Design: A rubber cover near the bottom of the water bottle meant to protect electrical components below. 2 weight sensors
above the rubber cover that measure the weight of the
water. Beagle Board that receives the weight information from
the sensors, records data every set time interval. Can send
information to a computer and light up green/red LEDS when prompted depending if the amount of water drunk is adequate level
Final Design: A grove water sensor attached to pocket beagle and other components that measures water. Other components include button, buzzer, 2 LEDS that will add user interactivity with the device. Water level will be measure every 30 seconds and based on that it will alert the user if they are below required intake
PocketBeagle
AIN
Computer
USB
GND
VCC
5V
GND
3.3V
GPIO
1k
Grove Water Sensor
SPI
GPIO
GND
VCC
3.3V
GPIO
GPIO
SPI
GPIO
AIN
USB
SPI
GPIO
GPIO
GPIO

## Slide 4: Mechanical Drawing
FRONT
BACK
Pocket Beagle
Groove water sensor
LEDS
Button
Buzzer